## Slide 1
BASIC ELECTRONICS
(24B11EC111)
Unit-1
Lecture-2
(Kirchhoff’s Laws)

## Slide 2: CONTENTS
Introduction
Kirchhoff’s Laws
  Kirchhoff’s Current Law (KCL)
  Kirchhoff’s Voltage Law (KVL)
Problems and solutions
Practice Problems
References

## Slide 3
Circuit
An electrical circuit is a closed path consisting of active and passive elements all interconnected and the current flow is confined to the closed path.
An active element is one which supplies energy to the circuit whereas passive element is one which receives energy and then this energy is converted into heat (resistor) or stores it in an electric (capacitor) or magnetic field (inductor).

## Slide 4
Power
Definition: Power is rate of doing work. It is the work done in unit time.
Equation of power is Eq1
where p is the power in watts, w is energy in joules, and t is time in seconds
The power associated with the current through an element is
From above equation it is clear, that power is simply the product of the voltage across an element times the current through the element. The power has units of watts and is denoted by W

## Slide 5: Energy
Definition: Energy is the capacity of doing work.
Equation of Energy: From eq1 by rewriting it
Eq 2
On integrating Eq 2, we have
SI unit of energy is joule and is denoted by ‘J’

## Slide 6: Power Received and Supplied by an element
Figure 1 (a)The element voltage and current adhere to the passive convention. (b) The element voltage and current do not adhere to the passive convention.
(a)
(b)
Figure 1 shows that there are two different ways to arrange the direction of the current and the polarity of the voltage.
Power Received
In Figure 1(a), the current is directed from the + toward the – of the voltage polarity. In this the voltage and current are said to “adhere to the passive convention.”
In the passive convention, the voltage pushes a positive charge in the direction indicated by the current.
The Power calculated is known as power received

## Slide 7: Contd..
Power supplied
In contrast, in Figure 1(b), the current is directed from the – toward the + of the voltage polarity.
In this case, the voltage pushes a positive charge in the direction opposite to the direction indicated by the current.
Accordingly, when the element voltage and current do not adhere to the passive convention, the power calculated by multiplying the element voltage by the element current is the power supplied by the element.
The power received by an element and the power supplied by that same element are related by

## Slide 8: SOURCES
Sources -devices that are intended to supply energy to a circuit. A source is a voltage or current generator capable of supplying energy to a circuit. An active two-terminal element that supplies energy to a circuit is a source of energy.
Sources are categorized as : voltage sources and current sources.

## Slide 9: INDEPENDENT SOURCES
Independent source: a voltage or current generator not dependent on other circuit variables.
Independent voltage source: provides a specified voltage independent of the current through it and is independent of any other circuit variable.
  For example, a voltage source specified by v(t) = 9 volts will have a voltage of 9 volts regardless of the circuit in which it is used. In contrast, the current of the voltage source depends on the circuit in which the source is used.
Independent current source: provides a current, independent of the voltage across the source element and is independent of any other circuit variable.
  For example, a current source specified by i(t) = —0.25 milliamps will have a current of —0.25 milliamps in any circuit in which it is used. The voltage across this current source will depend on the particular circuit.

## Slide 10: DEPENDENT SOURCES
Dependent sources model the situation in which the voltage or current of one circuit element is proportional to the voltage or current of the second circuit element.
  (In contrast, a resistor is a circuit element in which the voltage of the element is proportional to the current in the same element.)
Dependent sources are used to model electronic devices such as transistors and amplifiers. For example, the output voltage of an amplifier is proportional to the input voltage of that amplifier, so an amplifier can be modeled as a dependent source.
Fig. (a) shows a circuit that includes a dependent source represented by the diamond symbol. The plus/minus signs identify the dependent source as a voltage source and indicate the reference polarity of the element voltage.

## Slide 11
Current-Controlled Voltage Source (CCVS)
  r is the gain of the CCVS.
  r has units of volts/ampere.
Voltage-Controlled Voltage Source (VCVS)
  b is the gain of the VCVS.
  b has units of volts/volt.
Voltage-Controlled Current Source (VCCS)
  g is the gain of the VCCS.
  g has units of amperes/volt.
Current-Controlled Current Source (CCCS)
  d is the gain of the CCCS.
  d has units of amperes/ampere.
TYPES OF DEPENDENT SOURCES: SYMBOLS

## Slide 12: Kirchhoff’s Laws
In 1847, Gustav Robert Kirchhoff, a professor at the University of Berlin, formulated two important laws that provide the foundation for analysis of electric circuits. These laws are referred to as Kirchhoff’s current law (KCL) and Kirchhoff’s voltage law (KVL).
Kirchhoff’s laws are a consequence of conservation of charge and conservation of energy
Kirchhoff’s current law states that the algebraic sum (i.e taking reference directions into account) of the currents entering any node is identically zero for all instants of time.
  Kirchhoff’s current law (KCL): The algebraic sum of the currents into a node at any instant is zero.

## Slide 13
FIGURE (a) An electric circuit. (b) The same circuit, redrawn using straight lines and horizontal and vertical elements.
Figure (a) shows an electric circuit that consists of six elements connected together at four nodes.
It is common practice to draw electric circuits using straight lines and to position the elements horizontally or vertically as shown in Figure (b).
Kirchhoff’s Laws…

## Slide 14: Kirchhoff’s Current Law (KCL)
Consider the same circuit after labeling the nodes and elements.
Four elements of this circuit 1, 2, 3, and 4 are connected to node a.
By Kirchhoff’s current law, the algebraic sum of the element currents i1, i2, i3, and i4 must be zero.
Currents i2 and i3 are directed away from node a, so we will use a plus sign for i2 and i3. In contrast, currents i1 and i4 are directed toward node a, so we will use a minus sign for i1 and i4.
The KCL equation for node a
    -i1+i2+i3-i4 = 0
The circuit after labeling the nodes and elements.

## Slide 15: Kirchhoff’s Current Law (KCL)
An alternate way is to set the sum of all the currents directed away from the node equal to the sum of all the currents directed toward that node.
i2+i3= i1+i4
Similarly, the Kirchhoff’s current law equation for node b
i1 = i2+i3+i6

## Slide 16: Kirchhoff’s Voltage Law (KVL)
Kirchhoff’s voltage law (KVL): The algebraic sum of the voltages around any loop in a circuit is identically zero for all time.
The phrase algebraic sum indicates that we must take polarity into account as we add up the voltages of elements that comprise a loop.
One way to take polarity into account is to move around the loop in the clockwise direction while observing the polarities of the element voltages.
For example, consider the circuit shown in Figure c. Elements 3, 4, 5, and 6 comprise a loop of the circuit. By Kirchhoff’s voltage law, the algebraic sum of the element voltages v3, v4, v5, and v6 must be zero.
v4 - v5 - v6 - v3 = 0
Similarly, the KVL equation for
the loop consisting of (1, 4, 5, 6) is
v4 - v5 - v6 + v1 = 0
the loop consisting of (1 and 2) is
- v2 + v1 = 0

## Slide 17: Problems
Problem 1. Consider the circuit shown in Figure. Notice that the passive convention was used to assign reference directions to the resistor voltages and currents. This anticipates using Ohm’s law. Find each current and each voltage when R1 = 8 Ω, v2 = -10 V, i3 = 2 A, and R3 = 1 Ω. Also, determine the resistance R2.
Solution: The sum of the currents entering node a is
i1- i2- i3 =0
Using Ohm’s law for R3, we find that v3 = R3i3 = 1(2) = 2 V
Kirchhoff’s voltage law for the bottom loop incorporating v1, v3, and the 10-V source is
-10 + v1 + v3 = 0
Therefore; v1 = 10 - v3 = 8 V
Ohm’s law for the resistor R1 is v1 = R1i1
or i1 = v1/R1 = 8/8 = 1 A
Next, apply Kirchhoff’s current law at node a to get
i2 = i1 - i3 = 1-2 = -1 A
We can now find the resistance R2 from v2 = R2i2 or
R2 = v2/i2 = -10/-1 = 10Ω

## Slide 18: Problems
Problem 2. Determine the value of the current, in amps, measured by the ammeter in Figure a.

## Slide 19: Problems…
Solution:
An ideal ammeter is equivalent to a short circuit. The current measured by the ammeter is the current in the short circuit.
Figure b shows the circuit after replacing the ammeter by the equivalent short circuit.

## Slide 20: Problems…
Solution …
The circuit has been redrawn in Figure to label the nodes of the circuit. This circuit consists of a voltage source, a dependent current source, two resistors, and two short circuits. One of the short circuits is the controlling element of the CCCS, and the other short circuit is a model of the ammeter.
Applying KCL twice, once at node d and again at node a, shows that the current in the voltage source and the current in the 4Ω resistor are both equal to ia.
Applying KCL again, at node c, shows that the current in the 2Ω resistor is equal to im.

## Slide 21: Problems…
Solution …
Next, Ohm’s law tells us that the voltage across the 4Ω resistor is equal to 4ia and that the voltage across the 2Ω resistor is equal to 2im.
Applying KCL at node b gives
- ia -3ia - im = 0
Applying KVL to closed path a-b-c-e-d-a gives
0 = - 4ia + 2im -12 = -4(- im /4) + 2im - 12 = 3im - 12
Finally, solving this equation gives im = 4 A

## Slide 22: Problems…
Problem 3. Determine the value of the voltage, in volts, measured by the voltmeter in Figure a.

## Slide 23: Problems…
Solution:
An ideal voltmeter is equivalent to an open circuit.
The voltage measured by the voltmeter is the voltage across the open circuit.
Figure shows the circuit after replacing the voltmeter by the equivalent open circuit.
This circuit consists of a voltage source, a dependent voltage source, two resistors, a short circuit, and an open circuit.
The short circuit is the controlling element of the CCVS, and the open circuit is a model of the voltmeter.

## Slide 24
Solution …
The circuit has been redrawn in Figure to label the nodes of the circuit.
Applying KCL at node c, shows that the current in the 5Ω resistor is equal to the current in the open circuit, that is, zero.
Ohm’s law tells us that the voltage across the 5Ω resistor is also equal to zero.
Next, applying KVL to the closed path b-c-f-e-b gives vm = 3ia.
Applying KVL to the closed path a-b-e-d-a gives -4ia + 3ia -12 = 0
so ia = -12 A
Finally vm = 3ia = 3(-12) = -36 V
Problems…

## Slide 25: Practice Problem
Problem 1. Determine the values of i3, i4, i6, v2, v4, and v6 in Figure shown.
Answer: i3 = 3 A, i4 = 3 A, i6 = 4 A, v2 = 3 V, v4 = 6 V, v6 = 6 V

## Slide 26: REFERENCES
[1] R.C. Dorf and James A. Svoboda, “Introduction to Electric Circuits”, 9th ed, John Wiley & Sons, 2013.